Temperature controller Operation Manual

KC-671N                KC-871N

、Power On ( Input / Unit / Input Range )

①Power On  ②Input type  ③Input Range ④Degree

、Change Parameter Description

★Power On~A single button press, More than 60 seconds

、Default Value

| LEVEL | Parameter | Default value | Description |
| --- | --- | --- | --- |
| LEVEL 1 | AT |  | no | Auto Tuning |
|  | AL1 |  | 0 | Alarm Set Value |
| LEVEL 2 | P-1 |  | 3.0 | Proportional Band |
|  | I-1 |  | 120 | Integral Time |
|  | D-1 |  | 30 | Derivative Time |
|  | HYS |  | 1 | Out Hysteresis (±deviation value) |
|  | CY1 |  | 10 | Cycle Time 10sec REYLAY 1 sec SSR 0 sec 4-20MA |
|  | LOK |  | 0 | Level Function Lock |
| LEVEL 3 | INPT |  | K2 | Input type selection (refer ) |
|  | INLO |  | 0 | Input type AN- low calibration |
|  | INHI |  | 500 | Input type AN- high calibration |
|  | PVLO |  | 0 | PV set-Minimum point |
|  | PVHI |  | 400 | PV set-Maximum point |
|  | DP |  | 0 | Decimal point position |
|  | COLO |  | 300 | Out 4MA low calibration |
|  | COHI |  | 60 | Out 20MA high calibration |
|  | PVOS |  | 0 | PV low compensation |
|  | ALD |  | 0 | Alarm mode (refer ) |
|  | Id |  | 2 | Communications ID number |
|  | BUD |  | 9600 | Communications Baud Rate |
|  | SPT |  | 0 | MODBUS Communication protocol |
|  | SF |  | 300 | OUT Soft Filter |
|  | FIT |  | 5 | PV Filter |
|  | SFD |  | 0 | OUT Delay |

、Alarm Setting  ALD=0    Default Value No Alarm

| ALD | Alarm output operation | Description |
| --- | --- | --- |
| 0 | ---------------- | ■No alarm output |
| 1 |  | ■Deviation high-limit alarm If deviation between PV and SV is occurring higher than set value of deviation temperature, the output will be ON |
| 2 |  | ■Deviation low-limit alarm If deviation between PV and SV is occurring lower than set value of deviation temperature, the output will be ON |
| 3 |  | ■Deviation high/low-limit alarm If deviation between PV and SV is occurring higher or lower than set value of deviation temperature, the output will be ON |
| 4 |  | ■Deviation high-limit reverse alarm If deviation between PV and SV is occurring higher or lower than set value of deviation temperature, the output will be OFF |
| 5 |  | ■Absolute value high-limit alarm If PV is equal to or higher than the absolute value of alarm temperature, the output will be ON |
| 6 |  | ■Absolute value low-limit alarm If PV is equal to or lower than the absolute value of alarm temperature, the output will be ON |

、INPUT Type

| K | K1 | 0 ~ 99.9 | K2 | 0 ~ 400 |
| --- | --- | --- | --- | --- |
| J | J1 | 0 ~ 99.9 | J2 | 0 ~ 400 |
| PT100 | DP1 | 0 ~ 99.9 | DP2 | 0 ~ 400 |
| 4-20MA | AN1 | 0 ~ 99.9 |  |  |
| 1-5V | AN2 | 0 ~ 99.9 |  |  |